## Slide 1
WIS 2.0 Architecture
Enrico Fucile
Head, Data and Information Management Division
WIS 2.0 Training Workshop, Windhoek, Namibia, 20-24 March 2023​

## Slide 2
1963 World Weather Watch
1970s Global Telecommunication System
2007 WMO Information System (WIS)
2019 WMO Reform (Earth System Approach)
2021 WMO Unified Data Policy / GBON
WIS 2.0
… system of systems using Web-architecture and open standards to provide simple, timely and seamless sharing of trusted data and information …
  Internet and Web technologies
  Open Standards (OGC, W3C, IETF, …), royalty free
  Data sharing through Web and publication/subscription (pub/sub) protocols
  Cloud ready (turn-key solutions)
  Web APIs (Application Programming Interface)
WMO Information System (WIS 2.0)
Notes: A little history to start …
The WMO Global Telecommunications System (GTS), established in the 1970s was designed to enable WMO Members to share data and products with each other in support of operational weather forecasting. Over the last 40 years or so, the GTS has successfully moved indispensable, time-critical data between NMHSs day-in, day-out.
But weather and climate data is important to everyone. So WMO Congress commissioned the WMO Information System (WIS) in 2007.
WIS builds on and incorporates the GTS, adding a data catalogue, data discovery portal and additional mechanisms for users to subscribe to and download data shared on the GTS. It is comprised of hundreds of data providing centres from across the globe (Data Collection and Production Centres, and National Centres), plus 15 Global Information System Centres (or GISCs) that are regional hubs for search, discovery, and access to data.
The original WIS is a child of its time – designed circa 2005. It’s based on service-oriented architecture principles, uses complex ISO 19115/19139-based XML for metadata, and is not well integrated into the Web. Since 2005, we’ve seen a move towards “webby” applications, with good practice characterised in the W3C Data on the Web and W3C Spatial Data on the Web Best Practices. In summary: Resource-oriented architecture, RESTful Web services, and JSON and HTML as core formats.
This is a journey that OGC has been on for some time now, and many of the OGC API standards appear ripe for inclusion in WIS2.
Our aim for WIS2 is to increase data provider participation by lowering the technical barriers to entry, and from the data consumer perspective, make weather and climate data Findable, Accessible, Interoperable, and Reusable (FAIR).
---
Adoption of Internet enables people to make the best local choice for a connection – leveraging technology that is often commonly available and well understood
…
In many locations, Internet is reliable enough for safety critical applications – provided applications are built to be fault tolerant; may need to combine with [high-performance] managed networks to ensure quality of service (QoS)
GISCs operate Area Meteorological Data Communications Network (AMDCN) considering reliability, security, and availability – high-performance managed networks may be necessary
Software Defined Wide-Area Networks (SD-WAN) enable Internet and managed networks to be used together to provide reliable connectivity at reasonable cost
---
The core change for WIS 2.0 is use the Web to share data and information.
According to the World Wide Web Consortium (W3C) “the Web is the World’s most successful distributed information system.”
With Web technology at its core, WIS 2.0 will use widely adopted open standards and leverage industry best practices.
… Firstly, this will allow the global user community to conveniently discover, access and use authoritative weather, water and climate information.
… Secondly, it will be simpler for NMHSs to partner with others to deliver services to end-users due to sharing the same base technology.

## Slide 3
A message broker is a software that:
  implements one or more pub/sub protocols (Message Queuing Protocols)
  routes messages to one or more destinations
  allows content and topic-based message routing using the publish-subscribe pattern
What is a message broker?
Topic 1
Topic 2
User 1
User 2
User 3
Message BROKER
Publisher 1
Publisher 2
subscribe
subscribe
subscribe
subscribe
publish
publish

## Slide 4
AMQP | Choice of Aviation Beware of the version: 0-9-1 vs 1-0 ISO/IEC 19464:2014 (1.0)
MQTT 3.1 and 5.0 | WIS 2.0 MQP choice Initially for Internet of Things connectivity ISO/IEC PRF 20922
STOMP | Simple Text Oriented Messaging Protocol
JMS | Java only
Kafka | Broker (Apache Kafka) Data storage (Apache Zookeeper)
Redis | All in RAM Better on LAN level Data lost upon reboot
Some of the available protocols

## Slide 5
NCs / DCPCs must implement a WIS2 Node to exchange data in WIS2
The WIS2 Node shares data from an HTTPS service and sends notifications to MQTT subscribers
No need to provide access to all the users in the world, only to some WIS2 Global Services
WIS2 node is the WIS2 component providing data and associated metadata
WIS2 node replaces the GTS Message Switching System
Global
Services
WIS2 node
Subscribes to
Downloads data
Receives notifications of new data
WIS2 nodes and Global Services
Subscribes to
Receives notifications of new data
Downloads data

## Slide 6: Global Services
Global Cache
Global Discovery Catalogue
Global Broker
Global Monitoring
A storage providing a copy of the WMO Core data from the NCs/DCPCs to be accessed by the users.
  Data will be open to everyone.
  Some Global Caches are required globally for resilience.
Providing notifications of all the data available in the Global Caches or in originating centers.
  Users will subscribe to a Global Broker to get notifications of new data to be downloaded from Global Caches or WIS2 node
It is a discovery catalogue of data and services.
  Provides an API to list the available data and services
  Harvests metadata from the WIS2 Nodes.
Monitoring of data exchanged in WIS2.
  Sensor Centers will make available statistics from data in real time
  Global Monitoring Center will collect statistics from Sensor Centers and provide web accessible maps and results.
Discovers data/services
Subscribes to topics
Downloads core data
WIS2 node
Downloads recommended data

## Slide 7
Level | Name | Description
1 | channel | Location of where the data originates from (data providers [origin] or global services [cache])
2 | version | Alphabetical version of the topic hierarchy (currently a)
3 | system | Fixed value of wis2 for WIS2
4 | country | Lower case representation of ISO3166 3-letter code. Includes extensions for partner organizations
5 | centre-id | Acronym as specified by member and endorsed by the PR of the country and by WMO
6 | resource-type | WIS2 resources types (data, metadata, reports [from monitoring activities])
7 | data-policy | Data policy as defined by the WMO Unified Data Policy. core data are available from the Global Caches with open access on a free and unrestricted basis. Notifications for core and recommended data are available by subscription to Global Brokers. recommended data are downloaded from the original NC/DCPC and may require authentication/authorisation
8 | earth-system-discipline | As per Annex 1 of resolution 1 Cg-Ext-2021
9 | earth-system-discipline-category | As proposed by domain experts and further approved by INFCOM
WIS 2.0 topic hierarchy

## Slide 8
WIS 2.0 topic hierarchy examples
channel/version/wis2/country/centre-id/data/data-policy/earth-system-domain/subcategory/…
cache/a/wis2/arg/argentina_wmo_demo/data/core/weather/surface-based-observations/synop
cache/a/wis2/mar/casablanca_met_centre/data/core/weather/surface-based-observations/synop
cache/a/wis2/mar/casablanca_met_centre/data/core/weather/surface-based-observations/temp
cache/a/wis2/bfa/ouagadougou_met_centre/data/core/weather/surface-based-observations/synop
cache/a/wis2/cmr/yaounde_met_centre/data/core/weather/surface-based-observations/synop
cache/a/wis2/mwi/malawi_wmo_demo/data/core/weather/surface-based-observations/synop
cache/a/wis2/nga/abuja_met_centre/data/core/weather/surface-based-observations/synop
cache/a/wis2/gin/conakry_met_centre/data/core/weather/surface-based-observations/synop

## Slide 9
WIS 2.0 topic hierarchy examples
channel/version/wis2/country/centre-id/data/data-policy/earth-system-domain/subcategory/…
origin/a/wis2/arg/argentina_wmo_demo/data/core/weather/surface-based-observations/synop
origin/a/wis2/mar/casablanca_met_centre/data/core/weather/surface-based-observations/synop
origin/a/wis2/mar/casablanca_met_centre/data/core/weather/surface-based-observations/temp
origin/a/wis2/bfa/ouagadougou_met_centre/data/core/weather/surface-based-observations/synop
origin/a/wis2/cmr/yaounde_met_centre/data/core/weather/surface-based-observations/synop
origin/a/wis2/mwi/malawi_wmo_demo/data/core/weather/surface-based-observations/synop
origin/a/wis2/nga/abuja_met_centre/data/core/weather/surface-based-observations/synop
origin/a/wis2/gin/conakry_met_centre/data/core/weather/surface-based-observations/synop

## Slide 10
WIS2 Global Services
WIS2 Node
Data
WMO core data (free and unrestricted) can be downloaded from a Global Cache
Global Broker
Broker
download
subscribe
Global Cache
Notification of new data
download
WIS 2.0 supporting core data exchange
Notification of new data
subscribe
origin/a/wis2/…
cache/a/wis2/…
origin/a/wis2/…

## Slide 11
WIS2 Global Services
WIS2 Node
Data
Global Broker
Broker
download
subscribe
Global Cache
Notification of new data
download
WIS 2.0 supporting core data exchange
Notification of new data
subscribe
origin/a/wis2/…
cache/a/wis2/…
origin/a/wis2/…
WMO core data (free and unrestricted) can be downloaded from a Global Cache

## Slide 12
WIS2 Global Services
WIS2 Node
Data
Global Broker
Broker
subscribe
Global Cache
notification of new data
download
How a WIS2 Global Cache downloads data from WIS2 nodes
subscribe
notification of new data

## Slide 13
WIS2 Global Services
WIS2 Node
Data
WMO recommended data (can be restricted) shall be downloaded from a WIS2 Node
Global Broker
Broker
download
subscribe
subscribe
Global Cache
Notification of new data
Notification of new data
access control
WIS 2.0 supporting recommended data data and national needs
origin/a/wis2/…
origin/a/wis2/…

## Slide 14
WIS2 Global Services
WIS2 Node
Data
WIS2 Box is a reference implementation of a WIS2 Node
Global Broker
Broker
download
subscribe
subscribe
Global Cache
Notification of new data
Notification of new data
download
access control
download
BOX
WIS2 in a box

## Slide 15
Thank you
Merci